## Slide 1: STM32L4 MCU series Excellence in ultra-low-power with performance

## Slide 2: Agenda
Time
Presentation
    STM32L4 Family & Tools Overview
    Hands On Session: Out-of-the-box demos
    Hands On Lab#1: Getting Started with CubeMX and STM32L4
    STM32L4 Overview: Architecture, Memory, Clocks, Power
    Hands On Lab#2: printf() debugging via onboard ST-LINK
    STM32L4 Low Power details
    Hands On Lab#3: STM32CubeMX Power Consumption Calculator
    STM32L4 Peripherals Details 1/2
    Hands-On Lab#4: 3-axis MEMS Gyro communications
    STM32L4 Peripherals Details 2/2
    Hands-On Lab#5: Autonomous peripherals: ADC/TIM/DMA app
8:30 – 10:00

## Slide 3: Birth of the STM32 L4
STM32L4 is a perfect fit in terms of ultra-low power, performances, memory size, and peripherals at a cost effective price.
Convergence between High performance and Ultra-low power series
Ultra-low-power
Advanced analog,
New digital peripheral set
High-performance
ARM Cortex-M4 FPU, DSP

## Slide 4: Ultra-Low-Power and Flexibility
Down to 30 nA for I/O wake-up
with additional Shutdown mode
RTC available for all power modes
(from Active down to VBAT)
Down to 360 nA keeping 32 Kbytes of SRAM active
in Standby mode
Wake up MCU with any peripheral
(Communication I/Fs,
analog circuits, timers…)
External level shifter no longer needed
Separate VDD supplies
(down to 1.08 V)
I/O level kept in low power modes
Optimization of system consumption
USB capable with 32 kHz crystal oscillator
(Dedicated crystal oscillator is no longer needed for USB function)
4 nA VBAT mode with charging capability
Automatic switch to maintain power for RTC and backup registers
Internal oscillator from 100 kHz to 48 MHz (+/-0.25% int. clock accuracy over voltage/temperature with LSE)
1
STM32L4
STM32L4 is based on a new platform optimized to reduce power consumption and increase flexibility
FlexPowerControl
1
ULP leader and performance booster
Notes:   I/O level kept in low power modes
    Enable using a very low power modes while optimizing system consumption
    I/O level is maintained even during wake-up
  Backup SRAM in Standby mode
    32 kbytes can be kept
  Flexible wake-up sources in Stop mode
    I2C, UART, all I/Os, Low power Timers, RTC, Comparators, Reset pin, BOR, PVD, PVM, IWDG, OTG_FS, SWPMI
  Shutdown mode
    Down to 44nA with 5 I/O to wake-up
  Separated VDD supply
    14 I/Os with a dedicated supply (down to 1.08V): remove the need for external level shifter
  VBAT domain with charging capability
    Automatic switch to keep power on RTC and backup registers with internal charging circuitry
    3 tamper pins available in this mode
  MSI programmable from 100kHz to 48 MHz

## Slide 5: Ultra-low-power modes
Note : * without RTC / with RTC
1
Best power consumption numbers with full flexibility
RUN at 80 MHz 112 µA / MHz
Tamper: 3 I/Os, RTC
VBAT 4 nA / 300 nA*
Wake-up sources: reset pin, 5 I/Os,
RTC
SHUTDOWN 30 nA / 330 nA*
250 µs
Wake-up time
5 µs
Wake-up sources: + all I/Os, PVD,
LCD, COMPs, I²C, LPUART, LPTIM
STOP 2 (full retention) 1.1 µA / 1.4 µA*
Wake-up sources: any interrupt
or event
6 cycles
SLEEP 35 µA / MHz
RUN at 24 MHz 100 µA / MHz
4 µs
Wake-up sources: + all I²C, UART
STOP 1 (full retention) 7.3 µA / 7.6 µA*
14 µs
14 µs
Wake-up sources: + BOR,
IWDG
STANDBY 130 nA / 430 nA*
STANDBY + 32 KB RAM 360 nA / 660 nA*
1
ULP leader and performance booster

## Slide 6: STM32L4
Run 48 MHz
STOP mode
Run 80 MHz
< 5 µs!
  From 0 to 48 MHz in less than 5 µs
  From 0 to 80 MHz in less than 20 µs
www.st.com/stm32l4
153
273
100
Dhrystone
MIPS
And shatters performance limits in ULP world
On competition devices: discontinuity due to lack of DC/DC functionality when voltage decreases
No external coil and capacitor required for STM32L4
The higher the better!
This ULPBench® winner takes off like a rocket
Notes: The STM32L4 series shatters performance limits in the ultra-low-power world. It delivers 100 DMIPS (Di – Mips) based on its ARM® Cortex®-M4 core with FPU and ST’s ART Accelerator™ at 80 MHz. Once woken up from Stop mode, the internal clock is available in less than 5 µs running at 48 MHz and up to 80 MHz in less than 20 µs.
STM32L4 MCUs scored 153 in the standardized EEMBC™ ULPBench® tests that compare the efficiency of ultra-low-power microcontrollers. While competition is optimized at 3 volts, ST’s product delivers its full power efficiency at 1.8 volts. Since an external coil and capacitor are not required to reach this number, the BOM cost and the peak power consumption at start-up are reduced.

## Slide 7: High integration
Package size down
to 4.4 x 3.8 mm
High integration with high memory size in small packages
USB OTG,
1x SD/SDIO/MMC, 3 x SPI, 3 x I²C, 1x CAN, 1 x Quad SPI,
5 x USART + 1 x ULP UART,
1 x SWP
Connectivity
Cortex-M4 80 MHz FPU
MPU
ETM
Up to
1-Mbyte Flash with ECC
Dual Bank
128-Kbyte RAM
DMA
ART Accelerator™
AES (256-bit), TRNG, 2 x SAI, DFSDM (8 channels)
Digital
3 x 16-bit ADC, 2 x DAC,
2 x comparators, 2 x op amps
1 x temperature sensor
Analog
FSMC 8-/16-bit
(TFT-LCD, SRAM, NOR, NAND)
Parallel Interface
LCD driver 8 x 40
Display
17 timers including:
2 x 16-bit advanced motor control timers
2 x ULP timers
7 x 16-bit-timers
2 x 32-bit timers
Timers
I/Os
Up to 114 I/Os
Touch-sensing controller
3
Integration and safety

## Slide 8: Safety and security
Integrated safety and security features
Brown-out Reset
Clock Security System
SRAM parity check
Backup byte registers
Supply monitoring
Flash with ECC
Dual watchdog
SAFETY
ULP with
performance
SECURITY
Anti-tamper detection
Memory Protection Unit
Read and Write Protection
Unique ID
AES-256 Encryption
JTAG fuse
Random Number Generator
Software IP Protection
3
Integration and safety

## Slide 9
398 CoreMark
120 MHz
150 DMIPS
number of lines
608 CoreMark
180 MHz
225 DMIPS
High-performance
2
7
1
1 000 CoreMark
200 MHz
428 DMIPS
9 product series / 32 product lines
STM32L4 benefits from pin-to-pin compatibility across the family
STM32L4: continuity in STM32 portfolio
4
Great investment
Mainstream
106 CoreMark
48 MHz
38 DMIPS
4
177 CoreMark
72 MHz
61 DMIPS
5
245 CoreMark*
72 MHz
90 DMIPS
(*) from CCM-SRAM
6
Cortex-M0
Cortex-M0+
Cortex-M3
Cortex-M4
Cortex-M7
Ultra-low-power
75 CoreMark
32 MHz
26 DMIPS
3
93 CoreMark
32 MHz
33 DMIPS
3
273 CoreMark
80 MHz
100 DMIPS
1

## Slide 10: STM32L4 portfolio
4
Great investment
5
1 M / 128 K
512 K / 128 K
256 K / 128 K
LQFP64
(10x10x1.4 mm)
WLCSP72
(4.4x3.8x0.585 mm)
LQFP100
(14x14x1.4 mm)
UFBGA132
(7x7x0.6 mm)
LQFP144
(20x20x1.4 mm)
STM32L476RC
Flash memory / RAM size (bytes)
Pin count
STM32L476VC
STM32L476RE
STM32L476JE
STM32L476VE
STM32L476QE
STM32L476ZE
STM32L476RG
STM32L476JG
STM32L476VG
STM32L476QG
STM32L476ZG
STM32L486RG
STM32L486JG
STM32L486VG
STM32L486QG
STM32L486ZG
Legend:
With 128/256-bit AES hardware encryption
Without encryption
5
STM32L476ME
STM32L476MG
WLCSP81
(4.4x3.8x0.585 mm)
Notes: The STM32L4 portfolio is available in a wide choice of packages (from LQFP64 up to LQFP144) and from 256 Kbytes up to 1 Mbyte of Flash memory size.
The AES encryption hardware accelerator is optional.

## Slide 11: Hands-On Session: Out-of-the-box demos

## Slide 12
12
Motion Mems (9-axis)
Integrated ST-Link/V2-1 (for programming and debugging)
push buttons and joystick,
2 color LEDs
LCD 96 segments
USB OTG connector
Quad SPI NOR Flash
16 MB
STM32L476 Discovery – HMI

## Slide 13
13
MFX to auto-measure power
consumption
NFC / ACP connector
Microphone Mems
Direct access to all MCU I/Os
Audio Codec and 3.5 mm connector
STM32L476 Discovery - Audio and connector

## Slide 14: STM32L476 Discovery - back side
Flexible board power supply CR2032 battery or USB

## Slide 15: Out-of-the-Box Demos
Plug the USB cable into the top Mini-B connector of the Discovery Board
Use the blue joystick to scroll through the application menu:
  IDD Measurement app
  VDD Measurement app
  Record / Playback app
  Compass app
  Sound Meter app
  Guitar Tuner app
  Options
The project is in the CubeL4 library, Discovery Demonstrations folder:
  C:\Users\xxxx\STM32Cube\Repository\STM32Cube_FW_L4_V1.0.0\Projects\STM32L476G-Discovery\Demonstrations\EWARM
Notes: The RECORD application uses the MP34DT01 MEMS digital microphone to provide 16-bit audio samples at 48 KHz. The recorded audio file is stored into the QuadSPI Flash. Note that recording a new audio file will erase the previous one.
The PLAYER application plays back in loops any WAV file programmed in the internal Flash at address 8020000hex or stored in the QuadSPI Flash after a record; if both files are available, you can select from a sub-menu which one you want to play. It uses the CS43L22 on-board audio digital to analog converter to output the audio data on the 3.5 mm jack. Earphone volume can be adjusted during playback.

## Slide 16: IDD / VDD Measurement apps
Mode | Description
Run | Run 24Mhz, voltage range 2, PLL off, RTC/LSE off, Flash ART on
Sleep | Sleep 24Mhz, voltage range 2, PLL off, RTC/LSE off, Flash ART on
Low-power run | Low Power Run 2Mhz, PLL off, RTC/LSE off, Flash ART on
Low-power sleep | Low Power Sleep 2Mhz, PLL off, RTC/LSE off, Flash ART on
Stop 2 | RTC/LSE off, Flash ART off
Standby | RTC/LSE off, Flash ART off, RAM retention off
Shutdown | RTC/LSE off, Flash ART off
The “IDD Measure” app uses the “MFX” onboard STM32L151 as a non-intrusive auto-ranging current measurement probe.
The target L4 will enter a low power state, the MFX will measure the current, wake the L4 up and report the measurement back over I2C.
Notes: This menu allows to measure the current consumption in a subset of the STM32L4 low power capabilities.
First, select with the joystick the power mode (Run, Sleep, Low-power run, Low-power sleep, Stop 2, Standby or Shutdown) and the measurement will be displayed on the LCD.
Typically, you will observe that the STM32L476 consumes in the range of 1.3µA in Stop2 and 70nA in Shutdown under 3V at 25 degrees Celsius.
You may want to reuse the demonstration firmware to design your own low-power application.

## Slide 17: Audio demonstrations
RECORD application
  Uses MP34DT01 MEMS microphone (LED5 toggling during record)
  16-bit audio samples @ 48 kHz stored in N25Q128A13 QuadSPI Flash
  LEFT key to exit
PLAYER application
  Uses CS43L22 audio DAC and 3.5mm jack output
  Audio playback either from internal or QuadSPI Flash after a RECORD. Sub-menus :
    “FLASH” : Audio playback of any WAV binary file loaded @ 0x08020000
    “QSPI” : Audio playback from QuadSPI Flash
  Options :
    SEL key to pause/resume playback
    UP/DOWN keys to control volume
    Audio is played back in loops until LEFT key is pressed
Notes: The RECORD application uses the MP34DT01 MEMS digital microphone to provide 16-bit audio samples at 48 KHz. The recorded audio file is stored into the QuadSPI Flash. Note that recording a new audio file will erase the previous one.
The PLAYER application plays back in loops any WAV file programmed in the internal Flash at address 8020000hex or stored in the QuadSPI Flash after a record; if both files are available, you can select from a sub-menu which one you want to play. It uses the CS43L22 on-board audio digital to analog converter to output the audio data on the 3.5 mm jack. Earphone volume can be adjusted during playback.

## Slide 18: Compass and sound meter demonstrations
COMPASS application
  Uses LSM303C eCompass MEMS device
    3D accelerometer and 3D magnetometer
  Sub-Menu
    “CALIB”: rotate board (360° on all axis's) after scrolling message invitation
    “RUN”: displays angle in degrees
  LEFT key to exit
SOUND meter application
  Uses MP34DT01 audio sensor to measure ambient noise
  Displays measurement value in dB on LCD screen
  LEFT key to exit
Notes: The COMPASS application uses the on-board LSM303C eCOMPASS MEMS device to sense the earth magnetic field. The user needs to quickly rotate the board by 360 degrees on all 3 axis to perform the calibration step. The user can then enter the RUN sub-menu and observe the board angle in degrees.
The SOUND Meter application uses the on-board MP34DT01 digital microphone and displays the ambient noise in decibels.

## Slide 19: Guitar tuner demonstration
  Select guitar string
    “STR1”: “E” (low E, thickest string, closest to the ceiling)
    “STR2”: “A
    “STR3”: “D”
    “STR4”: “G”
    “STR5”: “B”
    “STR6”: “e” (high E, thinnest string, closest to the floor)
  RIGHT/SEL to start recording
  Output:
    “ ++ “ when string needs to be tightened
    “ + “ when string needs to be slightly tightened (close to correct tune)
    “ OK “ when string is correctly tuned
    “ - “ when string needs to be slightly loosened (close to correct tune)
    “ -- ” when string needs to be loosened
  LEFT key to exit
Notes: The GUITAR tuning application helps the user to tune his acoustic guitar. First select the string you want to tune and place the discovery board close to the sound hole. The sound is continuously recorded until valid samples are detected; the MCU then displays on the LCD screen whether the tune is correct or the string needs to be strained or loosen.

## Slide 20: Option app
1
1
ULP leader and performance booster
Select whether to enter STOP2 mode after few seconds of inactivity
Display Firmware version #

## Slide 21: Hands-On Lab #1: Getting Started with CubeMX LED Blinky in Five Easy Steps!

## Slide 22: Run STM32CubeMX

## Slide 23: Step 1: Create New Project
Create New Project
Select STM32L476VGTx
  LQFP100, 1024KB Flash
Click “OK”

## Slide 24: Step 2: Pin Configuration
In this example we are going to use the LED’s present on the STM32L476 Discovery board.
Left-click PB2 & PE8 and set to GPIO_Output mode

## Slide 25: Step 3: Generate Source Code
Open Project > Settings (Alt + P)
Set the project name (Lab1) and the project location (C:\STM32L4Seminar\Labs)
Set the IDE Toolchain to EWARM
Click OK
Generate Code (Ctrl + Shift + G)
Click Open Project

## Slide 26: Step 4: Toggle The LED
The IAR EWARM IDE should now be open.
Expand the file tree and open the main.c file
Add the following code inside the while(1) loop
  Line 85 in “main.c”
  Add within “USER CODE BEGIN WHILE” / “USER CODE END WHILE” section (this will preserve your code after regeneration)
HAL_GPIO_TogglePin(GPIOB, GPIO_PIN_2);
HAL_Delay(100);
HAL_GPIO_TogglePin(GPIOE, GPIO_PIN_8);
HAL_Delay(100);

## Slide 27: Step 5: Build the Project
Click “F7” or the “Make” button or use menu Project > Make.
Click the “Download and Debug” Green Arrow button (CTRL + D)
Click the “Go” button (F5)
Enjoy the flashing LED’s!

## Slide 28: In case it fails

## Slide 29: STM32L4 Overview Architecture, Memory, Clocks, Power

## Slide 30: STM32L476 block diagram
Notes: 26-Apr-16
30
All buses (AHB and APB) can operate up to 80MHz

## Slide 31: Flash organization
Two 512KB User Flash banks:
  Each bank is 256 pages of 2KB
Information block:
  System memory boot loader
  1 KB (128 double word) OTP for user data
  Option bytes for user configuration
Flash area |  | Flash memory address | Size | Name
Main memory | Bank 1 | 0x0800 0000 – 0x0800 07FF | 2K | Page 0
 |  | … |  | …
 |  | 0x0807 F800 – 0x0807 FFFF | 2K | Page 255
 | Bank 2 | 0x0808 0000 – 0x0808 07FF | 2K | Page 256
 |  | … |  | …
 |  | 0x080F F800 – 0x080F FFFF | 2K | Page 511
Information block | Bank 1 | 0x1FFF 0000 – 0x1FFF 6FFF | 28K | System memory
 | Bank 2 | 0x1FFF 8000 – 0x1FFF EFFF | 28K | 
 | Bank 1 | 0x1FFF 7000 – 0x1FFF 73FF | 1K | OTP area
 | Bank 1 | 0x1FFF 7800 – 0x1FFF 780F | 16 | Option bytes
 | Bank 2 | 0x1FFF F800 – 0x1FFF F80F | 16 | 

## Slide 32: Program / Erase
Parameter | Typ
64-bit programming time | 82 µs
Page (2 KB) erase time | 22 ms
One row (32 double-word) programming time | Normal : 2.6 ms Fast : 1.9 ms
One page (2 KB) programming time | Normal : 20.9 ms Fast : 15.3 ms
One bank (512 KB) programming time | Normal : 5.35 s Fast : 3.9 s
Mass erase time (1 or 2 banks) | 22 ms
ECC (Error Code Correction) : 8-bit for 64-bit word
  Single error correction:
    Failure address and bank saved in FLASH_ECCR register, optional interrupt
  Double error detection : NMI!
Programming granularity is 64-bit
Page granularity for erase is 2 Kbytes
Notes: Comparison with F4:
Double word programming : 16 µs
Sector (16 KB) erase : 230 ms
Sector (64 KB) erase : 490ms
Sector (128 KB) erase : 875ms
Mass erase : 6.9s

## Slide 33: Flash protections
Flexible Protections configurable with option bytes :
Readout protection (RDP)
  Forbids access to Flash/SRAM2/Backup registers by:
    Debug interface (JTAG/SWD)
    Boot from SRAM1
    Bootloader
Proprietary Code Protection (PCROP) with 64-bit granularity
  Used to protect specific code area from any read or write access
  The code can only be executed.
Write Protection (WRP) with 2-KByte granularity
  Used to protect specific code area from unwanted write/erase

## Slide 34: Readout Protections
Readout protection Level 0 : No read protection
    All operations are possible in all boot configurations.
Readout protection Level 1
    User mode: Code executing in user mode can access main Flash memory, option bytes, RTC backup registers and SRAM2 with all operations.
    Debug, boot RAM and boot loader modes: The main Flash memory, backup registers and SRAM2 are totally inaccessible in these modes, a simple read access generates a bus error and a Hard Fault interrupt.
  Un-protection, Level 1 to Level 0:
    Flash memory is mass-erased, RTC backup registers and SRAM2 are cleared
    If Option bit PCROP_RDP is set, the PCROP-protected area is not erased
Readout protection Level 2 (No debug)
    All protections provided by Level 1 are active.
    RAM boot, System memory boot and all debug features are disabled
    Option bytes can no longer be changed in user mode.
    Un-protection is not possible. It is an irreversible operation

## Slide 35: Proprietary Code (PCROP) / Write Protections
When enabled, PCROP area is protected against all D-code bus accesses
  The PCROP regions are execute-only
  1 area per bank, 64-bit granularity.
    PCROP area can be increased but never decreased
    Only way to deactivate PCROP is to change RDP from Level 1 to Level 0
Option bit PCROP_RDP
  When DISABLED: PCROP content is erased when RDP is changed from Level 1 to Level 0. PCROP_RDP is locked in this state.
  When ENABLED: PCROP content is preserved when RDP is changed from Level 1 to Level 0.
Flash Write Protection:
  Write-protected area is protected against erasing and programming.
  2 areas per bank, 2-KByte granularity.

## Slide 36: STM32 Firewall (FW)
The FIREWALL is made to protect parts of code/data (volatile and non volatile) from access from the rest of the code executed outside of the protected area.
GP-DMA
Cortex-M4
Bus Matrix
AHB/APB
SRAM1
FLASH
FIREWALL
Volatile Data
NVM code
NVM data
Reset event
3 Segments may be protected
by the Firewall
FW_CSSA
Start Address
Code Segment (NVM Code)
Protection : Code fetch
31
24
23
8
7
1
Length
FW_CSL
31
22
21
8
7
1
FW_NVDSSA
FW_NVDSL
Non-Volatile Data Segment (NVM Data)
Protection : Data
Start Address
31
24
23
8
7
1
Length
31
22
21
8
7
1
Volatile Data Segment (SRAM1 Data)
Protection: - Code fetch if SRAM1 is executable (not shared)
- Data
Start Address
FW_VDSSA
31
17
16
8
7
1
Length
FW_VDSL
31
22
21
8
7
1
FW_CR
FPA : Pre-alarm bit to control the exit point of the protected code
VDS : SRAM1 protected segment is sharable with non protected code
VDE : SRAM1 is executable into the protected volatile data segment
FPA
VDS
VDE
31
1

## Slide 37: Clocks: MSI (Multi-Speed Internal)
MSI = clock at startup from Reset, Standby or Shutdown modes.
12 Programmable frequency ranges:
  100 kHz, 200 kHz, 400 kHz, 800 kHz, 1 MHz, 2 MHz, 4 MHz (reset value), 8 MHz, 16 MHz, 24 MHz, 32 MHz, 48 MHz.
After Standby: Frequency selected from 1, 2, 4 or 8 MHz with MSISRANGE in RCC_CSR register.
Normal mode and PLL-mode (=auto-calibration with LSE)
  PLL-mode : allows USB FS device functionality (0.25% accuracy)
Factory and user trimmed

## Slide 38: HSI vs. MSI (design spec)
 | MSI |  | HSI
 | Normal mode | PLL-mode | 
Accuracy (max) | Over temperature: ±6% | Better than 0.25% | 0.3% after trim
 | Over voltage: From 100 to 800 kHz : ±1% From 1 to 8 MHz : ±2% From 16 to 48 MHz : ±4% |  | 
Consumption (typ) | 100 kHz : 0.5 µA |  | 130 µA
 | 800 kHz : 2µA |  | 
 | 1 MHz : 5µA |  | 
 | 8 MHz : 20 µA |  | 
 | 16 MHz : 60 µA |  | 
 | 48 MHz : 160 µA |  | 
Startup time (typ) | 100 kHz : 10 µs 48 MHz : 2.5 µs | 1.25 ms for 5% of final freq. | 0.9 µs

## Slide 39: Clocks: LSE (Low-Speed External)
LSE: programmable amplifier driving capability (4 modes)
  Available in all low-power modes + VBAT
Mode | Crystal (max) | Consumption (typ)
Ultra low power | 50kOhm/6pF | 200 nA
Medium low driving | 80kOhm/6pF | 260 nA
Medium high driving | 50kOhm/12.5pF | 410 nA
High driving | 80kOhm/12.5pF | 540 nA

## Slide 40: Clocks: LSI (Low-Speed Internal)
LSI 32kHz
  Available in all low-power modes except Shutdown and VBAT
Parameters | STM32L15x | STM32L4x
Accuracy over parts | 26..56KHz | ~8%
Accuracy over temperature | -10% / +4% (0..85°C) | 
 |  | 2% (-40 125°C)
Consumption (typ) | 400nA | 110nA

## Slide 41: Power schemes (1/3)
LCD
2 OPAMP
2 COMP
3 ADC
2 DAC
VREF buffer
VREF+
VDDA
VLCD
LCD booster
USB transceivers
VDDUSB
CPU
SRAM1
SRAM2
Digital peripherals
VCORE
VDD
I/O ring
VDDIO1
I/O ring
Flash
Voltage Regulator
Standby circuitry (wakeup, IWDG)
Reset block
Temp. sensor
3 PLL, HSI, MSI
VDDIO2
VDDIO2
Backup domain
LSE, RTC, backup registers
VBAT

## Slide 42: Peripheral Voltage Monitor
By default independent powers are electrically isolated and the features powered by them are not available
  The power isolation must be removed by SW
Peripheral Voltage Monitor for VDDA, VDDUSB, VDDIO2:
PVM | Power supply | PVM threshold | EXTI line
PVM1 | VDDUSB | VPVM1 = 1.2 V | 35
PVM2 | VDDIO2 | VPVM2 = 0,9 V | 36
PVM3 | VDDA | VPVM3 = 1.65 V | 37
PVM4 | VDDA | VPVM4 = 1.82 V | 38

## Slide 43: VCORE Voltage Regulator
Dynamic Voltage Scaling optimizes performance vs power
  VCORE Voltage Range 1 = 1.2V (Up to 80MHz)
  VCORE Voltage Range 2 = 1.0V (Up to 26MHz)
VCORE powered by main regulator (MR) or low-power regulator (LPR)
  MVR for Run and Sleep modes.
  LPR for LP run, LP sleep and STOP1/STOP2 modes.
  Regulators OFF in Standby and Shutdown mode.
    However LPR remains ON to preserve SRAM2 content in Shutdown mode, if required.
Notes: In Run mode, both MR and LPR are enable. Nevertheless the LPR startup time is longer than MR startup time, and when starting from BOR reset, Standby mode or Shutdown mode, the MCU starts before the LPR is woken up.
REGLPS flag shows when the LPR is ready

## Slide 44: Hands-On Lab #2: printf() debugging

## Slide 45
45
USART2 is routed to the ST-LINK’s USART, and brought via the USB Virtual-COM port class
(SB13/16 have been soldered)
Hands-On Lab #2 – printf() debugging
Adding to the existing CubeMX project, we will add USART2 debug via the ST-LINK Virtual-COM port
Set up additional GPIO / Clocks:
PD5 – USART2, “VirtualCOM-TX” – Alt. Fn. Push/Pull
PD6 – USART2, “VirtualCOM-RX” – Alt. Fn. Push/Pull
PA0 – GPIO_EXTI0: External Interrupt on Rising Edge Input
USART2 Clock = PCLK1 (80MHz)
USART2 settings:
Asynchronous Mode - 9600 N/8/1, No HW Flow control
Tx/Rx, 16-sample oversampling
No advanced features
User Code HAL function calls required:
See lab2_printf_debug.c in Lab2_Printf directory
Also Need Terminal emulator (Hyperterm, etc)

## Slide 46: GPIO Configuration additions
Expand the USART2 dialog, and select Asynchronous mode:
Use PD5 & PD6 for Tx / Rx pins:
  These are the alternate mapping pins (PA2/3 are default)
Use PA0 in External Interrupt Mode, Rising edge trigger:

## Slide 47: Clock Configuration
We will run the STM32L4 at 80MHz for this lab
Click on the Clock Configuration tab
  Set the PLL Source Mux to MSI
  Set the System Clock Mux to PLLCLK
  Use PLLM=/1, *N = x40, /R=/2
  AHB Prescaler = /1
  HCLK should equal 80MHz
80MHz

## Slide 48: USART2 Configuration
Click on the Configuration tab, and select USART2:
Parameter Settings tab:
  9600Bits/s
  8-bit word length
  No parity bit
  1 Stop bit
  Rx & Tx data
  16-clock oversampling
  No advanced feature settings needed
  No NVIC or DMA settings used

## Slide 49: NVIC Configuration
Click on the Configuration tab, and select NVIC:
Enable EXTI line0
Set Preemption Priority to 2
Click ‘OK’

## Slide 50: Regenerate Source Code for Lab1
Generate Code (Ctrl + Shift + G)
Open Project
Copy/Paste needed code bits for Hands-On Lab #2 into main.c:
  C:\STM32L4Seminar\Labs\lab2_printf_debug.c
    Add code bits between: /* USER CODE BEGIN PV */ /* USER CODE END PV */
    Add code bits between: /* USER CODE BEGIN 2 */ /* USER CODE END 2 */
    Add code bits between: /* USER CODE BEGIN WHILE */ /* USER CODE END WHILE */
    Add code bits between: /* USER CODE BEGIN 4 */ /* USER CODE END 4 */
  Open a terminal emulator, using USART2 settings, Virtual COM port xx
  Rebuild, Program/Debug, Run!

## Slide 51: STM32L4 Low Power details

## Slide 52: STM32L4 Power Mode Run mode
Low Power regulator (LPR)
up to 2MHz
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Range 1 (up to 80MHZ)
Run Mode Range 1
Ex: execution from Flash
Range 2
112uA/MHz at 26 MHz
(2.9 mA)
Range 1
131uA/MHz at 80 MHz
(10.2mA)
Active cell
Frozen cell
Main regulator (MR)
Available
Periph and clock
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QUADSPI
PVD, PVM
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Cell in power-down
GPIO
DMA
BOR
Range 2 (up to 26MHZ)

## Slide 53: STM32L4 Power Mode Low-power run mode
Low Power regulator (LPR)
up to 2MHz
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Range 1 (up to 80MHZ)
Range 2 (up to 26MHZ)
Low-power run mode
Ex: execution from Flash
From SRAM1
112 µA/MHz at 2 MHz
(225 µA)
from Flash
135 µA/MHz at 2 MHz
(269 µA)
Active cell
Frozen cell
Main regulator (MR)
Available
Periph and clock
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QUADSPI
PVD, PVM
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Cell in power-down
DMA
GPIO
DMA
BOR
FSMC
QUADSPI

## Slide 54: STM32L4 Power Mode Sleep mode
Low Power regulator (LPR)
up to 2MHz
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Range 1 (up to 80MHZ)
Sleep Mode Range 1
Ex: Flash ON, SRAMs ON (default)
Range 2
35 µA/MHz at 26 MHz
(0.92 mA)
Range 1
37 µA/MHz at 80 MHz
(2.96 mA)
Active cell
Frozen cell
Main regulator (MR)
Available
Periph and clock
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QUADSPI
PVD, PVM
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Cell in power-down
Zzz
DMA
GPIO
DMA
BOR
FSMC
QUADSPI
Range 2 (up to 26MHZ)

## Slide 55: STM32L4 Power Mode Low-power sleep mode
Low Power regulator (LPR)
up to 2MHz
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Range 1 (up to 80MHZ)
Range 2 (up to 26MHZ)
Low-power sleep mode
Ex: Flash OFF, SRAM1 OFF
Flash OFF, SRAMs OFF
40,5 µA/MHz at 2 MHz
(81 µA)
Flash ON, SRAMs OFF
48 µA/MHz at 2 MHz
(96 µA)
Active cell
Frozen cell
Main regulator (MR)
Available
Periph and clock
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QUADSPI
PVD, PVM
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Cell in power-down
Zzz
DMA
GPIO
DMA
BOR
FSMC
QUADSPI

## Slide 56: STM32L4 Power Mode Stop 1 Mode
Low Power regulator (LPR)
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Stop 1 w/ RTC on LSE quartz
Main regulator (MR)
Zzz
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QSPI
BOR
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Backup domain
RTC
Backup Register
(32x32-bits)
Wake-up
event
PVD
RTC + Tamper
LCD
USB OTG
USART
BOR
PVM
LP UART
I2C 1 / I2C 2
I2C 3
SWPMI
IWDG
GPIOs
COMP
LPTIM 1
LPTIM 2
7.1 µA @3.0V
6.9 µA @1.8V
DMA
PVD, PVM
6us wake-up from Flash
4us wake-up from RAM
GPIO
I/Os kept, and configurable
NRST

## Slide 57: STM32L4 Power Mode Stop 2 Mode
Low Power regulator (LPR)
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Stop 2 w/ RTC on LSE quartz
Main regulator (MR)
Zzz
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QSPI
BOR
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Backup domain
RTC
Backup Register
(32x32-bits)
Wake-up
event
PVD
RTC + Tamper
LCD
BOR
PVM
LP UART
I2C 3
IWDG
GPIOs
COMP
LPTIM 1
1.67 µA @3.0V
1.43 µA @1.8V
DMA
PVD, PVM
7us wake-up from Flash
5us wake-up from RAM
GPIO
I/Os kept, and configurable
NRST

## Slide 58: STM32L4 Power Mode Standby Mode
Low Power regulator (LPR)
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Standby
w/ SRAM2
w/o RTC
Main regulator (MR)
Zzz
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QSPI
BOR
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Backup domain
RTC
Backup Register
(32x32-bits)
Wake-up
event
RTC + Tamper
BOR
IWDG
5 WKUP pins
405 nA @ 3.0V
363 nA @1.8V
DMA
PVD, PVM
14 us wake-up
GPIO
I/Os can be configured
w/ or w/o pull-up
w/ or w/o pull-down
NRST

## Slide 59: STM32L4 Power Mode Standby Mode
Low Power regulator (LPR)
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Standby w/ RTC
on LSE quartz
Main regulator (MR)
Zzz
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QSPI
BOR
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Backup domain
RTC
Backup Register
(32x32-bits)
Wake-up
event
RTC + Tamper
BOR
IWDG
5 WKUP pins
650 nA @ 3.0V
433 nA@ 1.8V
DMA
PVD, PVM
14 us wake-up
GPIO
I/Os can be configured
w/ or w/o pull-up
w/ or w/o pull-down
NRST

## Slide 60: STM32L4 Power Mode Standby Mode
Low Power regulator (LPR)
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Standby
Main regulator (MR)
Zzz
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QSPI
BOR
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Backup domain
RTC
Backup Register
(32x32-bits)
Wake-up
event
RTC + Tamper
BOR
IWDG
5 WKUP pins
150 nA @ 3.0V
114 nA @ 1.8V
DMA
PVD, PVM
14 us wake-up
GPIO
I/Os can be configured
w/ or w/o pull-up
w/ or w/o pull-down
NRST

## Slide 61: STM32L4 Power Mode Shutdown Mode
Low Power regulator (LPR)
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Shutdown w/ RTC
on LSE quartz
Main regulator (MR)
Zzz
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QSPI
BOR
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Backup domain
RTC
Backup Register
(32x32-bits)
Wake-up
event
RTC + Tamper
5 WKUP pins
550 nA @ 3.0V
329 nA @ 1.8V
DMA
PVD, PVM
250 us wake-up
GPIO
I/Os can be configured
w/ or w/o pull-up
w/ or w/o pull-down
But floating when exit from Shutdown
NRST

## Slide 62: STM32L4 Power Mode Shutdown Mode
Low Power regulator (LPR)
SRAM 1 (96KB)
SRAM 2 (32KB)
Cortex M4
Flash
(1MB)
Shutdown
Main regulator (MR)
Zzz
USB OTG
SDMMC
SAI
Available
Peripheral
FSMC
QSPI
BOR
LCD
USART
LP UART
I2C 1 / I2C 2
I2C 3
SPI
CAN
ADC
DAC
OPAMP
COMP
SWPMI
DFSDM
Temp Sensor
Timers
LPTIM 1
LPTIM 2
Touch Sens
RNG
AES
CRC
IWDG
WWDG
Systick Timer
HSE
LSI
LSE
MSI
HSI
Available
Clock
Backup domain
RTC
Backup Register
(32x32-bits)
Wake-up
event
RTC + Tamper
5 WKUP pins
64 nA @ 3.0V
30 nA @ 1.8V
DMA
PVD, PVM
256 us wake-up
GPIO
I/Os can be configured
w/ or w/o pull-up
w/ or w/o pull-down
But floating when exit from Shutdown
NRST

## Slide 63: Low-power modes summary
Mode | Regulator | CPU | Flash | SRAM | Clocks | Peripherals In Bold : wakeup source | Consumption @ 1.8V | Wakeup time
Run | R1 | Yes | ON(1) | ON | Any | All | 131 µA/MHz | N/A
 | R2 |  |  |  |  | All except OTG, SDMMC, RNG | 112 µA/MHz | 
LPRun | LPR | Yes | ON(1) | ON | Any except PLL | All except OTG, SDMMC, RNG | 135 µA/MHz | TBD
Sleep | R1 | No | ON(1) | ON(2) | Any | All Any IT or event | 37 µA/MHz | 6 cycles
 | R2 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 35 µA/MHz | 
LPSleep | LPR | No | ON(1) | ON(2) | Any except PLL | All except OTG, SDMMC, RNG Any IT or event | 40 µA/MHz | 6 cycles
Stop 1 | LPR | No | OFF | ON | LSE/LSI | Reset pin, all I/Os BOR,PVD,PVM,RTC,LCD,IWDG, COMPx,DACx,OPAMPx,USARTx, LPUART,I2Cx,LPTIMx,OTG_FS, SWPMI | 6.6µA w/o RTC 6.9 µA w/RTC | 4 µs RAM 6 µs Flash
Stop 2 | LPR | No | OFF | ON | LSE/LSI | Reset pin, all I/Os BOR,PVD,PVM,RTC,LCD,IWDG, COMPx,LPUART,I2C3,LPTIM1 | 1.2 µA w/o RTC 1.4 µA w/RTC | 5 µs RAM 7 µs Flash
Standby | LPR | DOWN | OFF | SRAM2 ON | LSE/LSI | Reset pin, 5 WKUPx pins BOR, RTC, IWDG | + 235 nA | 14 µs
 | OFF |  |  | DOWN |  |  | 128 nA w/o RTC 433 nA w/RTC | 
Shutdown | OFF | DOWN | OFF | DOWN | LSE | Reset pin, 5 WKUPx pins RTC | 30 nA w/o RTC 329 nA w/RTC | 256 µs
Can be put in power-down and clock can be gated off
SRAM1 and SRAM2 can be gated off independently

## Slide 64: Low-power modes transitions
LPSleep
LPRun
Run
Stop2
Stop1
Sleep
Shutdown
Standby

## Slide 65: Hands-On Lab #3: Power Consumption Calculator

## Slide 66: Power Consumption Calculator Lab
Click on the Power Consumption Calculator tab in CubeMX
Select two AAA Alkaline batteries (in series) as our power source:

## Slide 67: Power Consumption Calculator Lab
Add a step to our power sequence: Click: Step.. Add
Configure a 10ms step:
  4.0MHz Range2 RUN mode
  GPIOB, GPIOE and USART2 peripherals enabled
  Click “Add”
  Resulting step consumption should be 762.8uA

## Slide 68: Power Consumption Calculator Lab
Add three more additional power steps:
  STOP2 mode, Battery power source, ALL Clocks OFF, 100ms duration
  LPRUN mode, FLASH fetch type, Battery power source, 2.0MHz freq, 5ms duration, GPIOB, GPIOE active
  Duplicate Step #2 (STOP2 mode) using the DUPLICATE button
Check the result:

## Slide 69: VBAT backup domain
VBAT charging : allows charging a super-cap on VBAT through internal resistor when VDD is present
  Battery charging is enabled by setting VBE bit in the PWR_CR4 register.
  VBRS bit value in the PWR_CR4 register selects the resistor value
VDD domain
1.5 kΩ
5 kΩ
Battery charging
VBAT
VDD
Backup domain
VBE
VBRS

## Slide 70: STM32L4 Peripheral details 1/2

## Slide 71: Smart peripherals Δ Metering
FSMC
External memory interface for static memories supporting SRAM, PSRAM, NOR and NAND
SPI / UART/ SDIO for Wireless
3x SPIs (4x SPIs with the Quad SPI)
6x USARTs (ISO 7816, LIN, IrDA, modem)
1 x SDIO
Anti Tamper pin
3 x tamper pins
for battery domain
I/Os Up to 114 fast I/Os for buttons & relays
TRNG & AES for Security
128-/256-bit AES
key encryption hardware accelerator
VBAT with RTC
for battery backup 240 nA in VBAT mode for RTC and
32x 32-bit backup registers
ADC
ΣΔ 24-bit
Digital Filter for Sigma
Delta Modulators
8 x parallel inputs
with up to 24-bit data output resolution
Electricity/Gas
/Water
Smart Meter
STM32L4
88×40 or 4×44
with step-up converter
LCD Display
2
Innovation
Notes: Pour FSMC remplacer l’image. On voit ecrit le nom d’un competitor dessus ;) « Spansion »

## Slide 72: Smart Peripherals Industrial Sensors
FSMC
External memory interface
for static memories supporting
SRAM, PSRAM, NOR and NAND
High temperature
from -40°C
up to + 125°C
SPI / UART
3x SPIs (4x SPIs with the
Quad SPI)
6x USARTs (ISO 7816, LIN,
IrDA, modem)
I/Os
Up to 114 GPIOs
STM32L4
CAN Bus
(2.0B Active)
Motor Control :
2x 16-bit advanced motor-control timers
3x 12-bit ADCs: 5 MSPS,
with up to 16-bit with hardware
oversampling, 200 μA/MSPS
I²C
3x I²C FM+(1 Mbit/s), SMBus/PMBus
TRNG & AES for Security
128/256-bit AES
key encryption hardware accelerator
8×40 or 4×44
with step-up converter
LCD Display
2
Innovation

## Slide 73: Smart peripherals Fitness tracker application
FSMC
Parallel interface to TFT
SPI
Up to 40 MHz speed
SPI / UART
3x SPIs
Quad SPI
6x USARTs
I²C
3x I²C FM+
Sensors
USB
USB OTG 2.0 full-speed,
LPM and BCD
Batch Acquisition Mode (BAM)
SWP
Single wire protocol master interface (SWPMI)
STM32L4
SAI
2x serial audio interfaces
Digital Filter for Sigma
Delta Modulators
with PDM microphone input support
TFT Display
OPAMP
2x with built-in PGA
DAC
Low-power sample and hold
ADC
3× 12-bit ADC 5 MSPS,
2
Innovation

## Slide 74: Smart peripherals - SPI
SPI
STM32L4
2
Innovation
Programmable frame from 4 to 16bit (bit granularity)
32-bit FIFO to optimize bus bandwidth (performance & power consumption)
BUSY status bit IP fix
Up to 40 Mbits/s in master mode
I2S functionality no longer supported in SPI. Now in SAI peripheral

## Slide 75: Hands-On Lab #4: SPI communications to MEMS Gyro

## Slide 76
76
Gyro (under LCD) data is routed to SPI2
Hands-On Lab #4 – SPI communications to 3-axis Gyro
Adding to the existing CubeMX project, we will add SPI communications to the L3GD20 MEMS gyroscope:
Set up additional GPIO / Clocks:
PD1 – SPI2 SCK – Alt. Fn. Push/Pull
PD3 – SPI2 MISO – Alt. Fn. Push/Pull
PD4 – SPI2 MOSI – Alt. Fn. Push/Pull
PD7 – nCS – GPIO Output, Push/Pull mode
SPI2 settings:
Full-Duplex Master
Motorola, 8-bit MSB-first
Prescaler /16
CPOL = Low, CPHA = 1-Edge
No CRC
Software NSS
User Code HAL function calls required to be added to main.c:
C:\STM32L4Seminar\Labs\lab4_spi_gyro.c

## Slide 77: Regenerate Source Code for Lab1
Needed code bits from C:\STM32L4Seminar\Labs\lab4_spi_gyro.c into main.c:
    Add code bits between: /* USER CODE BEGIN PV */ /* USER CODE END PV */
    Add code bits between: /* USER CODE BEGIN PFP */ /* USER CODE END PFP */
    Add code bits between: /* USER CODE BEGIN 2 */ /* USER CODE END 2 */
    Add code bits between: /* USER CODE BEGIN WHILE */ /* USER CODE END WHILE */
    Add code bits between: /* USER CODE BEGIN 4 */ /* USER CODE END 4 */
  Open a terminal emulator, using USART2 settings, Virtual COM port xx
  Rebuild, Program/Debug, Run!

## Slide 78: STM32L4 Peripherals details 2/2

## Slide 79: Smart peripherals - QuadSPI
QuadSPI
STM32L4
2
Innovation
Communication interface for single/dual/quad SPI flash memories

## Slide 80: Smart peripherals Sensor Hub scenario
SPI / UART
3x SPI
6x USART
I²C
Sensors
Batch Acquisition Mode (BAM)
STM32L4
2
Innovation
Host
App.
Processor
I²C
Wakeup from STOP
Optimized mode for transferring data while the system is in low power mode
Only the needed communication peripheral + 1 DMA + 1 SRAM (SRAM1 or SRAM2) are configured with clock enable in Sleep mode
Flash is in power-down mode
Enter either Sleep or Low-power sleep mode
  I2C clock can be at 16 MHz, allowing FM+ support

## Slide 81: Smart peripherals – USB OTG FS 2.0
USB
USB OTG 2.0 full-speed,
LPM and BCD
STM32L4
2
Innovation
USB 2.0 / OTG 2.0 compliant
VDDUSB: Dedicated 3.3V supply input
6 bidirectional endpoints
MSI in PLL mode (auto-trimmed with LSE) to reach 48MHz & < 0.25% accuracy
  HSE not needed
Link power management (LPM) support
  New power-save state, L1 (Sleep), with fast entry/exit compared to traditional L2 state (Suspend): 50uS vs 10mS
Battery charging detection (BCD) support
  Detect and identify the port type (standard or charging)
Attach Detection Protocol (ADP) support
  Allows an OTG device, embedded host or USB device to determine attachment status in the absence of bus power
Suspend/resume support
  Wakeup from STOP

## Slide 82: Smart peripherals
STM32L4
OPAMP
2x with built-in PGA
COMP
2x Low-power
DAC
2x Low-power sample and hold
ADC
3× 12-bit ADC 5 MSPS
2
Innovation
Analog Peripherals
OPAMP’s:
  Rail-to-rail inputs, 1mV offset after calibration
  Outputs: 500µA (sink/source), 100µA (low-power mode)
  1MHz GBW (normal mode), 500kHz (low-power mode)
  0.7V/µs slew rate (normal), 0.3V/µs (low-power Mode)
Comparators:
  2 Comparators
  Window mode
  Available in low-power modes
DAC’s:
  8/12-bit mode
  Lots of conversion triggers
  Programmable output buffer to drive more current
  Supply: VDDA = 1.8 V to 3.6 V
  NEW! Sample and hold low-power mode
ADC’s:
  ADC1/ADC2 are tightly coupled, ADC3 is standalone
  Consumption linear vs. conversion rate : 200 µA / MSPS
  Dual-clock architecture
  Up to 5.3Ms/s with 12-bit resolution in single mode
  Single-ended or differential inputs
  Internal channels: Temp sensor, VREF, VBAT/3, DAC
  NEW! Hardware Oversampling

## Slide 83: Sample & Hold feature
Maintains DAC output voltage when the MCU is in a low power mode, such as STOP1 mode
In Sample & Hold mode the DAC is able to hold its’ output voltage while all related analog and digital blocks are shut off
Up to 15x power savings in some configurations!
Vout
STM32L4
NEW!

## Slide 84: Oversampler
Oversampler performs data pre-processing to offload the CPU. Handles up to 256 conversions and averages them
  For : Averaging, Data rate reduction, SNR improvement, Basic filtering
Programmable oversampling ratio
  x2, x4, x8, x16, x32, x64, x128, x256
Programmable data shifting / truncating
  Right shift 0 to 8 bits
ADC
+
Accumulation data register
12bit data
DATA SHIFTER, TRUNCATER
20 bit register
ADCx_DR
16 bit register
0 to 8 bit right shift
CH1(0)
CH1(1)
CH1(0)
CH1(1)
Trigger for oversampling channel
Sampling
Conversion
EOC
Trigger
End of conversion for oversampling channel
Example: Oversampling ratio x2

## Slide 85: COMP low power features
Power consumption -vs- propagation delay can be adjusted:
LP mode | Feature / limitation
Run, LPRun | no limitation, state polling or interrupt thru EXTI
Sleep, LPSleep | wakeup capability thru EXTI
Stop 1, Stop 2 | wakeup capability thru EXTI
Standby | not available
Shutdown | not available
PWRMODE | Max propagation delay | Consumption (Typ)
00 | 80 ns | 70 µA
01 or 10 | 1 µs | 5 µA
11 | 12 µs | 350 nA

## Slide 86: LPTIM Features Summary
LPTIM: 00032
Asynchronous running capability
Ultra low power-consumption
Timeout function for wakeup from Stop 1 mode (LPTIM1 & LPTIM2) and Stop 2 mode (LPTIM1 only)

## Slide 87: LPTIM Features
Up to 5 clock sources to achieve lowest power consumption
  APB clock, LSE, LSI, HSI, External clock
Internal / External hardware triggers, with digital glitch filter:
  Rising / Falling or Both edges
  GPIO, RTC events, COMP1/2
Up to 2 operation modes
  Continuous mode: free running mode; many counter overruns are possible
  One Shot mode: Counter stops counting when the overrun value is reached
Encoder mode (LPTIM1 only)
6 interrupt sources

## Slide 88: LPTIM Features
Up to 3 configurable waveforms with configurable polarity
  PWM waveform
  One Pulse waveform
  Set Once waveform
PWM
OnePulse
SetOnce
POL = 0
LPTIMx_CMP
LPTIMx_ARR

## Slide 89: Hands-On Lab #5: Autonomous peripherals: ADC/TIM/DMA

## Slide 90
90
Internal L4 ADC / TIM / DMA peripherals
Hands-On Lab #5: ADC-TIM-DMA functionality
Set up additional GPIO / Clocks:
PA7 – ADC1_IN12 – Analog Input, Single-Ended
ADC Clock = SYSCLK/4 (20MHz)
PD15 – TIM4CH4 Alt Fn output – PWM Generation CH4
ADC1 settings:
Clock Prescaler = Synch /4
12-bit, Right aligned, No Scan, Scan/Continuous modes disabled
x16 oversampling, 4-bit shift, continued mode
Trigger on TIM4CC4, Rising edge
Enable DMA, 1 conversion
Channel 12: Rank1, 6.5 cycle sampling, no offset
DMA settings:
DMA1CH1, Circular mode, Increment memory address, Word data width
DMA1CH1 interrupt enabled, preempt priority = 3
TIM4 settings:
Counting UP, Prescaler=79, Counter Period = 1000, No CKD
PWM Mode 1, Pulse = 200, Fast Mode enabled, Polarity High
User Code HAL function calls required:
C:\STM32L4Seminar\Labs\lab5_adc_tim_dma.c

## Slide 91: TIM / ADC / DMA setup:

## Slide 92: Autonomous Peripherals
Needed code bits from C:\STM32L4Seminar\Labs\lab5_adc_tim_dma.c into main.c:
    Add code bits between: /* USER CODE BEGIN PV */ /* USER CODE END PV */
    Add code bits between: /* USER CODE BEGIN 2 */ /* USER CODE END 2 */
    Add code bits between: /* USER CODE BEGIN WHILE */ /* USER CODE END WHILE */
    Add code bits between: /* USER CODE BEGIN 4 */ /* USER CODE END 4 */
  Open a terminal emulator, using USART2 settings, Virtual COM port xx
  Rebuild, Program/Debug, Run!
On the rising edge of each TIM4 PWM cycle, the ADC is triggered.
The ADC input is oversampled 16 times
The summed result is shifted right 4 places, performing a hardware averaging
A DMA transfer moves this result into a data array and the array pointer is incremented
10 data elements are transferred and then the cycle repeats
Add the array ADC_Result to the Live Watch debug window to see updates!

## Slide 93: STM32 apps & social media
Find more about STM32 products and solutions:
ST MCU Finder mobile application
www.st.com/stmcufinder
Social media
  ST Forums on microcontrollers
  facebook.com/stm32
  youtube.com/STonlineMedia
  twitter.com/@ST_World
  Mbed.org
  STM32 @ ARM connected community
Notes: It has never been so easy to select, download, watch tutorials or get the [CLICK1] latest news about STM32 products and solutions on a computer, tablet or smartphone.
[CLICK2] The ST MCU Finder app lets you quickly and easily select the devices of your choice on a tablet or smartphone. Then, visit www.st.com/stm32. [CLICK3] The ST forums on microcontrollers allow the STM32 developer community to discuss and share experiences.
If you would like to know more about STM32 products and solutions in real-time, join the growing STM32 community on Facebook!

## Slide 94: Thank you
www.st.com/stm32l4
/STM32
@ST_World
st.com/e2e